Logic Design by MOS Gates

---
VLSI Design Flow
behavioral representation
Logic Synthesis
logic simulation
structural representation
Circuit Design
circuit analysis
Physical Synthesis
structural representation
extraction & verification
Fabrication
physical representation
specification
Function/architecture Design
System Specification
functional simulation
Packaging

---
Conduction Complement
Conduction Complement
Complementary CMOS gates always produce 0 or 1
Ex: NAND gate
  - Series nMOS: Y=0 when both inputs are 1
  - Thus Y=1 when either input is 0
  - Requires parallel pMOS
Rule of Conduction Complements
  - Pull-up network is complement of pull-down
  - Parallel -> series, series -> parallel
VDD
A
B

---
Realization by NAND Gates
AND-AND-OR-INV
Y
Y
C
D

---
CMOS Gate Design
CMOS Gate Design
CMOS NOR gate

---
Realization by NOR Gates
AND-AND-OR-INV
Y
Y

---
Complementary CMOS
(single complex cell)
Complementary CMOS
(single complex cell)
Complementary CMOS logic gates
  - nMOS pull-down network
  - pMOS pull-up network
  - a.k.a. static CMOS
X (crowbar)
0
Pull-down ON
1
Z (float)
Pull-down OFF
Pull-up ON
Pull-up OFF

---
Series and Parallel
Series and Parallel
- nMOS: 1 = ON
- pMOS: 0 = ON
- Series: both must be ON
- Parallel: either can be ON

---
Compound Gates
Compound gates can do any inverting function

---
Example:
Example:
LOAD
AB
LOAD
Y
Y
LOAD
CD

---
Example:
Example:
AB
Y
Y
CD
LOAD
LOAD
LOAD

---
Example:
Example:
LOAD
Y
Y
Y
LOAD

---
Several Realizations: NMOS
Several Realizations: NMOS
Y=AB + CD =AB + CD	=(A+B)(C+D)	=A C + B C + A D + B D
=(A +C)(B +C)(A +D)(B +D)
Series-Parallel (SP)
Parallel-Series (PS)

---
Several Realizations: PMOS
Several Realizations: PMOS
Y	= AB + CD = ( A+B ) ( C+D )= A C + B C + A D + B D
Parallel-Series (PS)
Series-Parallel (SP)

---
Different single complex cell designs using CMOS
Different single complex cell designs using CMOS
Y	= AB + CD
Y	= AB + CD
PS-PS
SP-PS

---
Different single complex cell designs using CMOS
Different single complex cell designs using CMOS
Y	= AB + CD
Y= AB+CD
SP-SP
PS-SP

---
How to optimize the circuit ?
The question of delay, power, space
Two level gate level optimization
Multilevel gate level optimization
Optimization with respect to transistors
Optimization with respect to space in fabrication of Integrated circuits