Layout and Stick Diagrams
Layout and Stick Diagrams

---
VLSI Design Flow
behavioral representation
Logic Synthesis
logic simulation
structural representation
Circuit Design
circuit analysis
Physical Synthesis
structural representation
extraction & verification
Fabrication
physical representation
specification
Function/architecture Design
System Specification
functional simulation
Packaging

---
Layout
Layout consists of creating appropriate masks that define the sizes and locations of sources, drains, gates, and the necessary interconnections
Layout is the lowest level of design abstraction for VLSI
Layout is directly sent to the manufacturer
Layout determines the circuit topology and the characteristics of components
Layout
Layout consists of creating appropriate masks that define the sizes and locations of sources, drains, gates, and the necessary interconnections
Layout is the lowest level of design abstraction for VLSI
Layout is directly sent to the manufacturer
Layout determines the circuit topology and the characteristics of components

---
MOSFET: Metal Oxide Semiconductor Field-Effect Transistor
n channel MOSFET
In lightly doped p-type substrate, two highly doped n regions (source and drain) are diffused
Insulator is grown over surface and holes are cut into it to have contact with source and drain
For Si substrate, SiO2 is used as the Insulator

---
Metal-Oxide-Semiconductor Field-Effect Transistor (MOSFET)
n-channel

---
NMOS

---
MOS Metalization process
It consists of three levels of conducting
material (Diffused region, polysilicon, metal )
Each layer is isolated from the
layers immediately above and below
Layers are color coded according to
different photolithigraphic masks needed
Metal
Oxide
Polysilicon
Poly
Oxide
Diffused
Bulk substrate
PMOS
Metal
Poly
Oxide
Diffused
Oxide
Bulk substrate
NMOS

---
MOS Metalization process
In some processes, there may be second metal layer
In some processes, a second polysilicon layer may exist
Layers may be joined together where contacts are formed
Metal
Oxide
Polysilicon
Poly
Oxide
Diffused
Bulk substrate
PMOS
Metal
Poly
Oxide
Diffused
Oxide
Bulk substrate
NMOS

---
Transistor Layout
Transistor Layout

---
n-well process
n-well process
MOSFET Layers in an n-well process
p-substrate
n+
n+
n+
n+
p+
p+
p+
p+
n-well
Gate
NMOS
NMOS
PMOS
PMOS
FOX

---
Layer Types
Layer Types
- p-substrate
- n-well
- n+
- p+
- Gate oxide
- Gate (polycilicon)
- Field Oxide
  - Insulated glass
  - Provide electrical isolation

---
Top view of the FET pattern
Top view of the FET pattern
PMOS
NMOS
NMOS
PMOS
n-well
n+
n+
n+
n+
p+
p+
p+
p+

---
Designing MOS Arrays
Designing MOS Arrays
A
B
C
y
x
B
C
A
y
x

---
Parallel Connected MOS Patterning
Parallel Connected MOS Patterning
x
x
A
B
A
B
X
X
X
y
y

---
Alternate Layout Strategy
Alternate Layout Strategy
x
x
X
X
A
B
B
A
X
X
y
y

---
Basic Gate Design
Basic Gate Design
- Both the power supply and ground are routed using the Metal layer
- n+ and p+ regions are denoted using the same fill pattern. The only difference is the n-well
- Contacts are needed from Metal to n+ or p+

---
The CMOS NOT Gate
The CMOS NOT Gate
Contact Cut
Vp
Vp
X
n-well
X
size 12{ {overline {x}} } {}
size 12{x} {}
size 12{ {overline {x}} } {}
X
size 12{x} {}
X
Gnd
Gnd

---
Alternate Layout of NOT Gate
Alternate Layout of NOT Gate
Vp
Vp
X
X
size 12{ {overline {x}} } {}
size 12{ {overline {x}} } {}
X
X
Gnd
size 12{x} {}
size 12{x} {}
Gnd

---
NAND2 Layout
NAND2 Layout
size 12{ {overline {a "." b}} } {} size 12{a} {} size 12{b} {}
Gnd
Vp
size 12{a} {} size 12{b} {}
size 12{ {overline {a "." b}} } {}
X
Vp
Gnd
X
X
X
X

---
NOR2 Layout
NOR2 Layout
size 12{ {overline {a+b}} } {} size 12{a} {} size 12{b} {}
Gnd
Vp
size 12{a} {} size 12{b} {}
size 12{ {overline {a+b}} } {}
Vp
Gnd
X
X
X
X
X

---
NAND2-NOR2 Comparison
NAND2-NOR2 Comparison
MOS Layout
Wiring
X
Vp
Gnd
X
X
X
X
X
X
X
X
X
Vp
Gnd

---
NAND2-NOR2 Comparison
MOS Layout
Wiring
X
Vp
Gnd
X
X
X
X
X
X
X
X
X
Vp
Gnd

---
General Layout Geometry
General Layout Geometry
Vp
Shared drain/
source
Individual
Transistors
Shared Gates
Gnd

---
Layout
Layout

---
Stick Diagrams
Stick Diagrams
Stick
Diagram
size 12{x} {} size 12{ {overline {x}} } {}
Gnd
VDD
size 12{x} {} size 12{ {overline {x}} } {}
X
X
X
X
VDD
Gnd

---
Stick Diagrams
size 12{x} {} size 12{ {overline {x}} } {}
Gnd
VDD
size 12{x} {} size 12{ {overline {x}} } {}
X
X
X
X
VDD
Gnd

---
Stick Diagrams
Stick diagrams help plan layout quickly
  - Need not be to scale
  - Draw with color pencils or dry-erase markers

---
Stick Diagrams
- VLSI design aims to translate circuit concepts onto silicon.
- stick diagrams are a means of capturing topography and layer information using simple diagrams.
- Stick diagrams convey layer information through colour codes (or monochrome encoding).
- Acts as an interface between symbolic circuit and the actual layout.

---
Stick Diagrams
Does show all components/vias.
It shows relative placement of components.
Goes one step closer to the layout
Helps plan the layout and routing
A stick diagram is a cartoon of a layout.

---
Stick Diagrams
Does not show
Exact placement of components
Transistor sizes
Wire lengths, wire widths, tub boundaries.
Any other low level details such as parasitics..

---
Stick Diagrams
Buried Contact
Contact Cut
Metal
poly
ndiff
pdiff
Can also draw
in shades of
gray/line style.

---
Stick Diagrams – Some rules
Stick Diagrams – Some rules
Rule 1.
When two or more ‘sticks’ of the same type cross or touch each other that represents electrical contact.

---
Stick Diagrams – Some rules
Rule 2.
When two or more ‘sticks’ of different type cross or touch each other there is no electrical contact.
(If electrical contact is needed we have to show the connection explicitly).

---
Stick Diagrams – Some rules
Rule 3.
When a poly crosses diffusion it represents a transistor.
Note: If a contact is shown then it is not a transistor.

---
Stick Diagrams
Stick Diagrams
Rule 4.
For depletion mode transistor put a yellow rectangle
Enhancement type	Depletion type
Feature Symbol:

---
Examples of NMOS Stick layout Design Style
VDD
Vout
Vin
NMOS Inverter
VDD
Vout
Vin
8:1
1:1
VDD
GND
VDD
GND
8:1
1:1
VDD
GND
CK
Input
Output
Bounding Box

---
Examples of NMOS Stick layout Design Style: Realizing a logic function X= A + BC
VDD
Vout
Vout
Vin
VDD
GND
4:1
1:2
VDD
GND
1:2
4:1
1:2
GND
1:2
VDD
A
1:1
C
(B)
Bus
X
Bounding Box

---
Stick Diagrams – Some rules
Rule 5.
In CMOS a demarcation line is drawn to avoid touching of p-diff with n-diff. All pMOS must lie on one side of the line and all nMOS will have to be on the other side.
Feature Symbol:
NMOS	PMOS

---
How to draw Stick Diagrams
Stick Diagrams
How to draw Stick Diagrams

---
Stick Diagram – Example
NOR Gate
OUT
B
A

---
Stick Diagram - Example
Power
Ground
C
Out
A
B

---
Example: 1 bit shift register
1
2
VDD
VDD
2
1
VSS
VSS
Demarcation line
VDD
VSS
VDD
VSS
VDD
VSS
Data input
Data output

---
Example: 1 bit shift register
VDD
1
2
VDD
VDD
2
1
VSS
VSS
VSS
Data input
Data output
VDD
VSS
Data input
1
1
2
2
Data output

---
Stick Diagram to Symbolic Form: CMOS shift Register
VDD
1
1
2
2
VSS
VDD
VSS
1
1
2
2
Data input
Data output
Data input
Data output

---
Stick Diagram to Symbolic Form: CMOS shift Register
VDD
VSS
Data input
1
1
2
2
Data output
Can be merged
VDD
VSS
Data input
1
1
2
2
Data output
c
d
a
b

---
Points to Ponder
be creative with layouts
sketch designs first
minimize junctions but avoid long poly runs
have a floor plan plan for input, output, power
 and ground locations

---
Layout Comparison
Layout Comparison
Which layout is better?