Design Rules

---
Design Rules
Design Rules
- Allow translation of circuits (usually in stick diagram or symbolic form) into actual geometry in silicon
- Interface between circuit designer and fabrication engineer
- Compromise
  - designer - tighter, smaller
  - fabricator - controllable, reproducable

---
Design Rules - The Reality
Design Rules - The Reality
- Manufacturing processes have inherent limitations in accuracy and repeatability
- Design rules specify geometry of masks that provide reasonable yield
- Design rules are determined by experience

---
Problems - Manufacturing
Problems - Manufacturing
- Photoresist shrinking / tearing
- Variations in material deposition
- Variations in temperature
- Variations in oxide thickness
- Impurities
- Variations across the wafer

---
Problems - Manufacturing
Problems - Manufacturing
Variations in threshold voltage
  - oxide thickness
  - ion implantation
  - poly variations
- Diffusion - changes in doping (variation in R, C)
- Poly, metal variations in height and width -> variation in R, C
- Shorts and opens
- Via may not be cut all the way through
- Undersize via has too much resistance
- Oversize via may short

---
Meta Design Rules
Meta Design Rules
- Basic reasons for design rules
- Rules that generate design rules
- Under worst case misalignment and maximum edge movement of any feature, no serious performance degradation should occur

---
Advantages of Generalised Design Rules
Advantages of Generalized Design Rules
- Ease of learning because they are scalable, portable, durable
- Longevity of designs that are simple, abstract and minimal clutter
- Increase designer efficiency
- Automatic translation to final layout

---
Lambda Based Design Rules
Lambda Based Design Rules
- Design rules based on single parameter, λ
- Simple for the designer
- Wide acceptance
- Provide feature size independent way of setting out mask
- If design rules are obeyed, masks will produce working circuits
- Minimum feature size is defined as 2 λ
- Used to preserve topological features on a chip
- Prevents shorting, opens, contacts from slipping out of area to be contacted

---
DESIGN RULES
Thin Oxide
n diffusion
p diffusion
2
3
1
2
Polysilicon
2
2
Metal 1
Metal 2
3
4
3
4
3
4

---
Thin Oxide
n diffusion
Metal 1
p diffusion
2
3
3
3
3
Metal 2
1
2
4
2
4
2
4
Different widths	Value
Diffusion Region width	2
Polysilicon region width	2
Diffusion-Diffusion spacing	3
Poly-Poly spacing	2
Polysilicon gate extension	2
Contact extension	
Metal width	3
Basic nMOS design Rules
Polysilicon

---
DESIGN RULES
2
6 X 6
2 X 2
2 X 2
2
nMOS enhancement
pMOS enhancement
nMOS depletion

---
DESIGN RULES
2
6 X 6
2 X 2
2 X 2
2
nMOS enhancement
pMOS enhancement
nMOS depletion

---
DESIGN RULES
Size Rules
The minimum feature size of a device or interconnect is determined by the line patterning capability of lithographic equipment
Design rule must specify the minimum feature sizes on different layers to ensure a valid design of a circuit
Separation Rules
Different features on the same layer or in different layers must have some separations from each other
Most IC processes have a spacing rule for each layer and several rules for interlayer spacing

---
DESIGN RULES
Overlap rules
Design rules must protect against fatal errors
Example of Fatal errors
      - A short circuited channel caused by mismigration of poly or diffusion
       - The formation of an enhancement mode FET in parallel with depletion device
       - Misregistration of ion-implant area and source/drain diffusion
Incorrectly formed
Correctly formed

---
DESIGN RULES
2
Separation from contact cut to transistor
Implant for an nMOS depletion mode transistor to extend 2 minimum beyond channel in all directions
2
2
Separation from implant to another transistor
2
Diffusion is not to decrease in width < 2 from polysilicon
2
Polysilicon to extend minimum 2 beyond diffusion biundaries

---
Overlap rules for contact cuts: nMOS and CMOS
4
Metal to Polysilicon
2
4
3
2
4
3
2
Metal to Diffusion
2

---
Overlap rules for contact cuts : nMOS and CMOS
4
2
4
3
2
2
2
Multiple Contact cuts

---
Overlap rules for contact cuts and via : nMOS and CMOS
Cut means connection to source , drain and poly, while via is used to make connection between 2 metal layers
2
via
        Via:
- Contact from metal2 to metal 1
- Contact through other layer
Metal 2
Cut
Metal 1
 Via and cut used to connect metal2 to diffusion
Metal 2 to diffusion
via
cut

---
Design rules: NMOS
VDD
It is sometimes advantageous to connect polysilicon to diffusion
Output
Input
Two basic contacts are there for these contacts
(1) Butting contact
(2) Buried Contact

---
Butting Contact: nMOS
4
6

---
Butting Contact: nMOS
2
2
2
Implant to extend 2 in all directions beyond channel
2
Channel Length L
Pull up transistor in nMOS

6



4

---
Butting Contact
SiO2
p type substrate
n diffusion

---
Buried Contact: nMOS
Layers are joined over a 2 X 2 area with the buried contact cut extending by 1
to all directions around the contact area
(But the contact cut extension is 2 in diffusion paths leaving the contact area)
2
2
1
2
1
2
1
1
2
1
1
Follow separation rule
Unrelated polysilicon or diffusion

---
Buried Contact (nMOS pull up)
Implant to extend 2 in all directions beyond channel
2
2
Implant
2
Channel Length L
2
4
Buried Contact
(4 X 4)


4

---
Buried Contact: Cross Section
p type substrate
n diffusion
SiO2

---
NMOS Inverter: Circuit-stick diagram-mask
VDD
VDD
Zpu=2:1
Wpu
Output
Lpu
Input
Zpd=1:2
Implant
Buried contact
Output
VDD
Wpd
Zpu=2:1
Input
Lpd
Output
GND
Zpd=1:2
Input
GND

---
Metal2-via-Metal1-cut-ndiffusion connection
p type substrate
n diffusion
cut
SiO2
via
Metal 2
Metal 1

---
Design Rules: p-well CMOS
Vout
Vss
N+ for N-substrate contact)
P+ (for P-substrate contact)
P
pMOS
P+
N+
p well
nMOS
N-type substrate
to n-type features
p well
p+ mask
4
2
Metal
VSS
2
VSS contact to p-well


2
3
4
4
Vdd
Vin

---
Design Rules: p-well CMOS
to n-type features
p well
p+ mask
Metal
VSS
VSS contact to p-well
Can be merged into single split contact

3
2

4
3
2
4
p well
p+ mask
to n-type features
Metal
VSS
VSS contact to p-well
3
2

2

---
Design Rules: p-well CMOS
Vout
Vss
N+ for N-substrate contact)
P+ (for P-substrate contact)
P
pMOS
P+
N+
p well
nMOS
3
4
2
2
2
Metal
VDD
4
2
VDD contact to substrate
to p-type features
Vdd
Vin

---
Design Rules: p-well CMOS
2
VDD
Metal
VDD contact to substrate
to p-type features
Can be merged into single split contact
4
2
4
Metal
VDD
3
2

VDD contact to substrate
to p-type features
2

---
Design Rules: p-well CMOS
Split contacts may also be made with separate cuts
VSS
VDD
4
2
2
4
2

---
Design Rules: p-well CMOS
5
External Thinox
S = 2 minimum for wells at same potential
   = 6 minimum for wells at different potentials
4
p-well must overlap all enclosed thinox by 3 minimum
Thinox must not cross well boundary

---
Design Rules: p-well CMOS
Separation between two p+ masks
Spacing from unrelated thinox
2
2
2
2
2
Overlap of thinox
Separation to channel

---
Aspects related to vias
2
Separation via to via
Overlap by metal1

2
2
Separation via to polysilicon
2
Separation via to thinox

---
Polysilicon wire separation from cuts
2
Short polysilicon run
3
Long polysilicon run
6
5
Diffusion wire separation from cuts
Separation between different active areas

---
Polysilicon wire separation from cuts
Increase in polysilicon overlap
Polysilicon is to be extended in direction of metal
2
2
2

---
Example: 1 bit shift register: Circuit to stick diagram
1
2
VDD
VDD
2
1
VSS
VSS
VDD
VSS
1
1
2
2
Data input
Data output
Data input
Data output

---
Stick Diagram to Symbolic Form: CMOS shift Register
VDD
1
1
2
2
VSS
VDD
VSS
1
1
2
2
Data input
Data output
Data input
Data output

---
Stick Diagram to Symbolic Form: CMOS shift Register
VDD
VSS
Data input
1
1
2
2
Data output
Can be merged
VDD
VSS
Data input
1
1
2
2
Data output
c
d
a
b

---
Symbolic Form to Mask form: CMOS shift Register
p+ mask
p well
VDD
VSS
Data input
1
1
2
2
Data output
c
d
a
b