Partitioning

---
VLSI Design Flow
System Specification
specification
functional simulation
Function/architecture Design
logic simulation
behavioral representation
Logic Synthesis
circuit analysis
structural representation
Circuit Design
structural representation
extraction & verification
Physical Synthesis
physical representation
Fabrication
Packaging

---
Physical Design
Physical Design

---
Circuit Partitioning
Circuit Partitioning

---
Why Partitioning?
Partitioning-The process of decomposition of a large system into independent manageable subsystems.
Why partition a circuit ?
•Complex system with a large number of components
•Efficient design by breaking into smaller subsystems
•Each subsystem can be designed independently and concurrently
•Decompose the system so as to preserve the original functionality
•Minimize interface across the partition
•Time for decomposition should be small
The Goal: To improve the circuit performance and reduce the layout cost

---
Partitioning
•Decomposition of a complex system into smaller subsystems
–Done hierarchically
–Partitioning done until each subsystem has	manageable size
–Each subsystem can be designed independently
•Interconnections between partitions minimized
–Less hassle interfacing the subsystems
–Communication between subsystems usually costly

---
Hierarchical Partitioning
•Levels of partitioning:
–System-level partitioning:
  Each sub-system can be designed as a single PCB
–Board-level partitioning:
  Circuit assigned to a PCB is partitioned into sub-circuits each fabricated as a VLSI chip
–Chip-level partitioning:
 Circuit assigned to the chip is divided into
 manageable sub-circuits
 NOTE: physically not necessary

---
VLSI Layout can be represented by a graph
VLSI Layout
Graph Representation

---
Circuit Partitioning: A Graph-Theoretic Problem
1
5
2
6
3
7
8
4
cut cost = 9
cut cost = 1
1
2
3
4
5
6
7
8

---
Circuit Partitioning Complexity
Circuit Partitioning Complexity
- For 2n circuit nodes, # of possibilities = (2n)
- For a 100-gate circuit, there are 5 1028 possibilities;
    It will take around 1.59 x 1013 years if one checks
    100 M possibilities per second.
n

---
Graphs and Hypergraphs
The input Circuit of a VLSI Physical Design problem is a hypergraph
a
h
b
g
c
f
d
e
Graph
Hyperedge
a
b
c
d
e
f
Hypergraph

---
Graphs and Hypergraphs
It is difficult to design efficient algorithms based on hypergraph
Thus a circuit is usually transformed to a graph before algorithms are applied

---
Procedure Hypergraph-transform
Begin
for each hypergraph e (M1, M2, ……… Mn) do
(i) form a complete graph G with vertices (M1, M2, ……… Mn);
weight of an edge (Mi, Mj) is proportional
to the number of hyperedges of the circuit
between (Mi,Mj);
(ii) find a minimum spanning tree T of G
(iii) replace e with the edges of T in the original hypergraph
endfor
end
Several algorithm exist to represent hyperedges with graph edges, but most effective one is still unknown

---
Books
N. A Sherwani
Algorithms for VLSI physical design automation
M Sarrafzadeh and C K Wong
An Introduction to VLSI Physical Design