Floorplanning-3

---
Floorplan sizing problem
The circuit models can usually be implemented in different sizes
Each module has many implementations with different size, speed, and power consumption trade off
The floorplan sizing problem is actual module implementation
If a cell has only one implementation, it is called a fixed cell

---
Floorplan sizing problem
Assume a fixed cell environment
b
a
2
b
4
d
1
a
c
d
e
3
c
2
e
1
3
4
Horizontal dependency graph
Floorplan
Maximal vertical segments
Horizontal dependency graph:
- A directed acyclic graph
- The length of each edge is the width of the corresponding	module in the floorplan
- The longest path from leftmost to rightmost segment is	the minimum width of the chip
The height of the chip can be determined by vertical dependency graph

---
Hierarchical Floorplan Sizing
Consider variable cells on a sliceable floorplan
Given:
      A sliceable floorplan F, and for each module Mi, a set of possible implementations of the module, where each implementation is described by a pair of real numbers (wk, hk) representing width and height of module
If a module has the realizations (w1, h1), (w2, h2), (w3, h3), ……….., the realizations of are sorted in a manner such that wp < wq and hp> hq for all p < q
For wp <wq if hp ≮hq, exclude (wq, hq) from the list
 If a module Mi has si realizations, then
w1< w2 < w3,……… <wsi, and
h1> h2 > h3,……… >hsi,

---
Hierarchical Floorplan Sizing
Lemma: Given two subfloorplans corresponding to two subtrees of a node v, one with t and other with s nonredundant implementations, then v has at most s+t-1 nonredundant realizations
v
L
R
Procedure vertical node sizing
Input: Two sorted lists L= {(a1,b1), (a2,b2), …….,(as,bs)}, and R= {(x1,y1), (x2,y2), ………..,	(xt,yt)}, where ai<aj, bi>bj, xi,<xj, yi>yj for all i < j
Output: A sorted list H= {(c1,d1), (c2,d2), …….,(cu,du)}, where ci<cj, di>dj, for all i < j
H= Ø, i=1, j=1, k=1
while (i ≤s) and (j≤ t) do
(ck, dk)= (ai+ xj, max(bi, yj); H= H ⋃(ck, dk); k=k+1
if max(bi, yj)= bi, then i=i+1;
   if max(bi, yj)= yj, then j=j+1;

---
Hierarchical Floorplan Sizing: Algorithm
Input: A binary tree corresponding to floorplan with leave nodes representing the modules
Output: Complete floorplan
From each leaf node traverse the tree up to root
by vertical node sizing procedure
The sizing algorithm runs in O(dn) time, where n is the number of modules and d is the height of the the slicing tree
For a balanced binary tree, d= logn
In the worst case, d=n

---
Linear Programming Technique
Nonhierarchical floorplan sizing method
No restriction on the organization of modules
Notation
(wi,hi)	: width and height of module Mi
(xi,yi)	: coordinates of the lower left corner of module Mi
(x,y)	: width and height of the final floorplan
(ai,bi)	: min and max values of the aspect ratio wi/hi of module Mi
For any module Mi, ai≤ wi/hi ≤ bi
Usually, ai= 1/bi
The solution is to find (xi, yi, wi, hi) such that all constraints are satisfied and xy is minimized

---
Linear Programming Technique: Constraints
For any two modules Mi and Mj
Nonoverlap constraint
xi+wi ≤ xj (Mj is to the right of Mi), or
xj+wj ≤ xi (Mj is to the left of Mi), or
yi+hi ≤ yj (Mj is to the above of Mi), or
yj+hj ≤ yi (Mj is to the below of Mi)
At least one of the above constraints must be satisfied
(xj, yj)
(xi, yi)
(xj, yj)
(xi, yi)
(xj, yj)
(xi, yi)
(xi, yi)
(xj, yj)

---
Linear Programming Technique: Constraints
Nonoverlap constraint
xi+wi ≤ xj (Mj is to the right of Mi), or
xj+wj ≤ xi (Mj is to the left of Mi), or
yi+hi ≤ yj (Mj is to the above of Mi), or
yj+hj ≤ yi (Mj is to the below of Mi)
At least one of the above constraints must be satisfied
For each pair (Mi , Mj), pij (0 or 1) and qij (0 or 1) are introduced
W and H = upper bounds of the width and height of feasible solution region
xi+wi ≤ xj + W(pij + qij)
xj+wj ≤ xi + W(1- pij + qij)
yi+hi ≤ yj + H(1+ pij - qij)
yj+hj ≤ yi+ H(2- pij - qij)
The above system of inequalities solves the overlap constraint

---
Linear Programming Technique: Constraints
Module size constraint
Consider that the blocks are not of fixed sizes
For each module Mi, a lower bound on area Ai and aspect ratios ai,bi are given, s.t., wihi ≥ Ai , and ai ≤ wi /hi ≤ bi
wmin =√Aiai, wmax =√Aibi, hmin =√Ai/bi , hmax =√Ai/ai
h
hi=Δiwi + ci
Δi-= (hmax - hmin ) /(wmin - wmax)
ci=hmax - Δi wmin
hmax
hi=Δiwi + ci
The ineuqualities to be solved
xi+wi ≤ xj + W(pij + qij)
xj+wj ≤ xi+ W(1- pij + qij)
yi+ Δiwi +ci ≤ yj + H(1+ pij - qij)
yj+ Δjwj +cj ≤ yi+ H(2- pij - qij)
wihi = Ai
hmin
w
wmin
wmax

---
The Cost function
The function to be minimized = the total area of the floorplan A= xy
Let us fix the width W and minimize the height of floorplan
min y
xi+wi ≤ W
 y ≥ yi+hi

---
Complete LP formulation
The function to be minimized = the total area of the floorplan A= xy
Let us fix the width W and minimize the height of floorplan
min y
xi, wi , yi ≥ 0
pij, qij =0 or 1
xi+wi ≤ W
 y ≥ yi+hi
xi+wi	≤ xj + W(pij + qij)
xj+wj	≤ xi + W(1- pij + qij)
yi+ Δiwi +ci	≤ yj + H(1+ pij - qij)
yj+ Δjwj +cj	≤ yi+ H(2- pij - qij)