Semiconductors
Semiconductors

---
Conductivity of materials
Conductivity is proportional to the concentration n of free electrons
A good conductor:	n ≈ 1028 electrons / m3
An insulator:	n ≈ 107 electrons / m3
semiconductors are materials which have a conductivity between conductors and nonconductors or insulators
Semiconductors are made from pure elements, typically silicon or geranium, or compounds such as gallium arsenide.

---
Conductivity is caused by movement of free electrons
Electrons are moving around the nucleus in different shells
Shells are divided in subshells
The maximum no of electrons that be present in a shell or subshell is fixed
Electron shell and subshells
shell	K	L		M			N
n	1	2		3			4
l	0	0	1	0	1	2	0	1	2	3
subshell	s	s	p	s	p	d	s	p	d	f
No of Electrons	2	2	6	2	6	10	2	6	10	14
	2	8		18			32

---
Who are semiconductors?

---
Availability of free electrons is dependent on the element
Electronic configuration in Group IV A
Element	Atomic number	Configuration
C	6	1s2 2s2 2p2
Si	14	1s2 2s2 2p63s2 3p2
Ge	32	1s2 2s2 2p63s2 3p63d104s2 4 p2
Sn	50	1s2 2s2 2p63s2 3p63d104s2 4 p64d105s2 5p2
C, Si, Ge, Sn are in same Group IV A in periodic table
Each has completely filled subshells except for outermost p subshell having only two of six possible electrons
C in crystalline form: an insulator
Si, Ge: semiconductors
Sn: metal

---
Most metals and semiconductors are crystalline in structure
Diamond Lattice
Tetrahedral structure
4 nearest neighbors
A crystal consists of a space array of atoms built up by regular repetition in three dimensions of some fundamental structural unit
The characteristics at any point is the result of contributions from every atom

---
A crystal consists of a space array of atoms built up by regular repetition in three dimensions of some fundamental structural unit
The characteristics at any point is the result of contributions from every atom

---
Most metals and semiconductors are crystalline in structure
The energy levels of inner shell electrons are not affected appreciably by the presence of neighboring atoms
The levels of the outer shell electrons are changed considerably, since they are shared by more than one atom in the crystal

---
Energy Band Theory of Crystals
If atoms are far away, interaction between them is negligible, energy levels coincide with those of isolated atom
As no of atoms per cm3 is very large (~1023), the total spread between minimum and maximum energy may be several electron volts (energy band)
Energy
Interatomic spacing
Inner shell atomic energy levels unaffected by crystal formation
Imagine that the spacing between atoms may vary
If interatomic spacing decreases,
(i) An atom will exert an electric force on its neighbors.
(ii) The crystal becomes an electronic system (follow Pauli exclusion principle)
(iii) s and p states spread out in energy
Energy band

---
Energy Band Theory of Crystals
For small enough distance
(i) the bands overlap
(ii) each atom gives up 4 electrons;
These electrons can no longer be in s or p subshell, they belong to the crystal as a whole
Energy
Interatomic spacing
The band these electrons occupy is called as valence band
Valence band

---
Energy Band Theory of Crystals
Energy
Interatomic spacing
Crystal lattice spacing
Behavior follows Schrodinger’s equation
At the crystal lattice spacing a0, valence band is filled with 4 electrons separated by a forbidden band (no allowed energy state) of extent Eg from an empty band
The upper vacant band is called conduction band
If interatomic spacing decreases further, say below the distance at which the bands overlap, the interaction between atoms become very large
The energy band structure becomes dependent upon
(i) orientation of the atoms relative to another in space (crystal structure)
(ii) atomic number
Eg

---
Energy Bands in Semiconductors
Energy Bands in Semiconductors
Let there be N atoms in the crystal
The space between the bands is the energy gap, or forbidden band

---
Energy Band Structure
Conduction band
The large forbidden band
For diamond (carbon) crystal, Eg ≈ 6ev
The energy that can be supplied to an electron is too small to carry it to conduction band from the filled into valance band
Valence band
The small forbidden band. Behaves like insulator at low temperature
Eg = 0.72 (1.21) ev for Ge (Si) at room temperature
Energies of this magnitude cannot be supplied by an electric field
If the temperature increases, some elctrons from valence band jump into the empty conduction band to become free electrons
The absence of an electron in valence band creats a hole
Free electrons
Holes
Conduction band
Valence band
Semiconductor
No forbidden band.
Valence band merges into empty band
Under influence of an electric field the elctrons acquire additional energy and move into higher energy states to constitute a current
Conduction band
Valence band
Metal
Eg ≈ 6ev
Eg ≈ 1ev
Insulator

---
Electrons and holes in semiconductor
Crystal structure of semiconductor consists of a space array of atoms built up by regular repetition in three dimensions of a unit cell having the form of an tetrahedron
For ease of understanding, let the crystal structure of semiconductor is symbolically illustrated in two dimensions
Si
Si
Si
The inert core of Si atom carries a positive charge of + 4
Each of the valence electron of a Si atom is shared by one of its nearest neighbours
This electron pair forms covalent bond
Valence becomes tightly bound to nucleus
At low temperature (say 00 K), the crystal becomes an insulator
Si
Si
+4
+4
+4
Si
Si
+4
+4
+4
Si
+4
+4
+4
Si
Si
Si
Si
Si

---
Electrons and holes in semiconductor
At room temperature, some of the covalent bonds will be broken
Some electrons may be dislodged to become free to wander in random fashion throughout the crystal
Absence of electron in covalent bond is called a hole
When a hole exists, a valence electron in neighboring atom may leave its covalent bond to fill this hole – thus the hole moves
This hole in new position may now be filled by an electron from another covalent bond, causing further movement of hole
free electron
hole
Si
Si
Si
Si
Si
+4
+4
+4
Si
Si
+4
+4
+4
Si
+4
+4
+4
Si
Si
Si
Si
Si
Conduction of electricity is possible without involving free electrons

---
Donor impurity in semiconductor
free electron
Si
Si
Si
A small amount of impurity with 5 valence electrons is added
Four of five valence electrons occupy covalent bonds, the fifth is unbound and becomes free
The type of impurity is donor, as it donates electrons
It is called n-type semiconductor
Suitable pentavalent impurites: P, Sb, As
Si
Si
+4
+4
+4
P
Si
+4
+5
+4
Si
+4
+4
+4
Si
Si
Si
Si
Si
Allowable energy levels are introduced a very small distance [(0.01 {0.05} ev for Ge {Si}),] below conduction band
This new allowable level is discrete, as added impurity atoms are far apart in crystal structure, their interaction is small
Energy required to detach this fifth electron from atom to raise it in conduction band is only 0.01 {0.05} ev for Ge {Si},
The presence of large no of electrons increases rate of recombination of holes and electrons, thus decreases the no of holes below that is available in intrinsic semiconductor
Conduction band
Donor energy level
Valence band
n-type Semiconductor
Eg ≈ 1ev
Ev
Ec
Ed

---
Acceptor impurity in semiconductor
hole
Si
Si
Si
A small amount of impurity with 3 valence electrons is added
Three valence electrons fill three covalent bonds, a vacancy exists in 4th bond, creating a hole that can accept electron
The type of impurity is acceptor, as it accepts electrons
It is called p-type semiconductor
Suitable trivalent impurites: B, Ga, In
Si
Si
+4
+4
+4
In
Si
+4
+3
+4
Si
+4
+4
+4
Si
Si
Si
Si
Si
Allowable energy levels are introduced which is just above valence band
This new allowable level is discrete, as added impurity atoms are far apart in crystal structure, their interaction is small
Very small amount of energy is required for an electron to leave valence band and occupy acceptor energy level
The presence of large no of holes increases rate of recombination of holes and electrons, thus decreases the no of electrons below that is available in intrinsic semiconductor
Conduction band
Acceptor energy level
Valence band
p-type Semiconductor
Eg ≈ 1ev
Ev
Ec
Ea

---
Result of doping in semiconductor
Increases conductivity
Produces conductors in which electric carriers are either predominantly holes or predominantly electrons
In n-type semiconductor, majority carrier is electrons and minority carrier is holes
In p-type semiconductor, majority carrier is holes and minority carrier is electrons
By combining n-type and p-type semiconductors materials that conduct only under certain conditions can be created