Semiconductors
Semiconductor Devices

---
Semiconductor Diode
Junction
Acceptor ion
Donor ion
holes
electrons
p type
n type
Donor and acceptor impurities are introduced in two sides of a single crystal of semiconductor
By donating an electron a donor impurity atom becomes a positive ion
An acceptor impurity atom becomes a negative ion after accepting an electron
Holes diffuse to the right and electrons to the left across the junction
As holes and electrons combine across the junction, they disappear near the junction
+
+
+
+
-
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

---
Semiconductor Diode
Junction
Donor ion
Acceptor ion
holes
electrons
p type
n type
0.5 cm
An electric field appears across the junction
Equilibrium is established, when field is large enough to restrain the process of diffusion
For further movement of holes and electrons, they have to cross a potential barrier (i.e. we have to apply an external field)
Unneutralized ions in the neighborhood of the junction are uncovered charges
The region across is called space charge region or depletion region
Thickness of depletion region is very small (10-4 cm)
+
+
+
+
-
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

---
P-N Junction – Forward Bias
P-N Junction – Forward Bias
- positive voltage placed on p-type material
- holes in p-type move away from positive terminal, electrons in n-type move further from negative terminal
- depletion region becomes smaller - resistance of device decreases
- voltage increased until critical voltage is reached, depletion region disappears, current can flow freely
+

---
P-N Junction – Reverse Bias
P-N Junction – Reverse Bias
- positive voltage placed on n-type material
- electrons in n-type move closer to positive terminal, holes in p-type move closer to negative terminal
- width of depletion region increases
- allowed current is essentially zero (small “drift” current)
+

---
IV Characteristics of Diode

---
Semiconductor Transistor
n-type semiconductor is sandwiched between two layers of p-type
p-type semiconductor is sandwiched between two layers of n-type

---
Bipolar Junction Transistor (BJT)
base
base
n	p n
p	n p
Flow of holes
Flow of electrons
Currents flow mainly due to majority carriers
Emitter
collector
Emitter
collector

---
Reference positive directions for both NPN and PNP transistors.
Reference positive directions for both NPN and PNP transistors.

---
An npn transistor with variable biasing sources (common-emitter configuration).

---
Base characteristic with collector-to-emitter voltage constant.
Base characteristic with collector-to-emitter voltage constant.

---
Collector characteristics of an ideal representative BJT.
Collector characteristics of an ideal representative BJT.

---
Three regions of operation for a BJT.
Amplification occurs in the active region. In saturation, vCE < 0.2 V.

---
Modes of Operation
Modes of Operation
Common-emitter output characteristics
(IC vs. VCE)
Mode	Emitter Junction	Collector Junction
CUTOFF	reverse bias	reverse bias
Forward ACTIVE	forward bias	reverse bias*
Reverse ACTIVE	reverse bias*	forward bias
SATURATION	forward bias	forward bias
*or not strongly forward biased

---
Models to assist in visualizing BJT as two diodes.
Models to assist in visualizing BJT as two diodes.

---
Ideal model of BJT in cutoff region.
Ideal model of BJT in cutoff region.

---
Ideal model of BJT in saturation region.
Ideal model of BJT in saturation region.

---
Transistor as an amplifier.

---
Transistor Amplifier Basics
Transistor Amplifier Basics
ib
+
IB
=
iB
0

---
Load-line analysis

---
Load-line analysis of the amplifier

---
Voltage waveforms for the amplifier

---
BJT switch using an NPN transistor.
BJT switch using an NPN transistor.