Field Effect Transistors

---
Transistor problems
Transistor problems
- Power density increased
- Device variability
- Reliability
- Complexity
- Leakage
- Power dissipation limits device density
- Transistor will operate near ultimate limits of size and quality – eventually, no transistor can be fundamentally better
◄

---
Junction FETs (JFETs)
Junction FETs (JFETs)
- A piece of semiconductor material which constitutes a channel
- Conducting semiconductor channel between two ohmic contacts – source & drain
The Symbol

---
n type bar acts as a simple semiconductor resistor
Electrons flow from Source to drain if an electric field is applied between them
Only one carrier – electrons (for n-channel) or holes (for p channel) - unipolar
Depletion region exists for p-n junctions
Due to depletion region, the conduction portion of channel constricts
Channel thickness is dependent on both VDS and VGS

---
Electrons flow from source to Drain
Current ID flows through channel
For a fixed VDS, ID is also dependent on VGS as it increases or decreases the reverse bias
Mechanism of current is the effect of field produced by VDS and VGS (FIELD EFFECT TRANSISTOR)
ID
VGS
VDS

---
I-V characteristics
I-V characteristics
More VGS (more –ve) implies
      - More reverse bias
      - More depletion region
      - Less channel width
      - Less current ID

---
Characteristics in linear portion of the ohmic region.
Current ID flows through channel following Ohm’s law
VDS

---
The structure of a n-Channel FET
At any point a, voltage = V- IR
R is dependent on distance from drain.
The constriction is more pronounced at distance farther from the source
The constriction is dependent on the current (which is dependent on both VGS and VDS)

---
Junction FETs (JFETs)
Junction FETs (JFETs)
Length of Depletion region depends on the reverse bias voltage
Length of Depletion region depends on the voltage difference between channel and gate
The voltage at channel is dependent on position , as ohmic drop varies along the channel
Thus the constriction of conduction channel is not uniform

---
The structure of a n-Channel FET
ID
VGS
VDS
For a fixed VGS, if increase VDS more and more, ID will increase, - and channel will constrict more and more
Eventually ID is reached to such a level (IDSS) such that the channel is pinched off
At this point ID begins to level off and approach a constant value
pinch-off voltage, VP , which is the value of VDS at which the maximum IDSS flows
Note: channel never completely closes as that reduces ID to zero

---
I-V characteristics
I-V characteristics

---
FET output characteristics

---
Increasing more and more reverse bias (VDS ) causes the junctions to breakdown
If VGS is more negative, the breakdown occurs at early VDS

---
More practical n-channel JFET
Difficult in diffusing impurities into both sides of a semiconductor
(a)
Single-ended-geometry junction FET
Diffusion is from one side only
N-type channel is epitaxially grown in p-type substrate

---
Depletion layer thickness is changing with VDS

---
Bipolar Junction Transistor versus Field Effect Transistor
FET is unipolar. – there is only majority carrier. BJT is bipolar (there are both majority and minority carrier)
No offset voltage at zero drain current
High input resistance
Has thermal stability
Less noisy
Relatively immune to radiation
Simpler to fabricate and takes less space in integrated form