Metal Oxide Semiconductor Field-Effect Transistor

---
MOSFET: Metal Oxide Semiconductor Field-Effect Transistor
n channel MOSFET
In lightly doped p-type substrate, two highly doped n regions (source and drain) are diffused
Insulator is grown over surface and holes are cut into it to have contact with source and drain
For Si substrate, SiO2 is used as the Insulator

---
Metal-Oxide-Semiconductor Field-Effect Transistor (MOSFET)
n-channel

---
(+)
MOSFET operation
Substrate: Grounded
Gate : + ve voltage
+ + + + + + + + + + + + +
_ _ _ _ _ _ _ _ _ _
+ + + + + + + + + + + +
- - - - - - - - - - - -
An electric field is directed perpendicularly through oxide
Negative charge is induced on semiconductor
A channel is formed between drain and source
Width of channel depends on gate voltage
Induced channel

---
Electrons may flow through Channel

---
Basic Operation
1) Source and substrate grounded (zero voltage)
2) (+) voltage on the gate
Attracts e-s to Si/SiO2 interface; forms channel
3) (+) voltage on the drain
e-s in the channel drift from source to drain
current flows from drain to source

---
MOSFET
Metal-oxide-semiconductor field-effect transistor
G = gate, D = drain, S = source, B = body (substrate)

---
N enhance FET at Pinchoff
N enhance FET at Pinchoff

---
Drain characteristics for an ideal representative N-channel enhancement-mode MOSFET.

---
Terminal Voltages
Terminal Voltages
Mode of operation depends on Vg, Vd, Vs
  - Vgs = Vg – Vs
  - Vgd = Vg – Vd
  - Vds = Vd – Vs = Vgs - Vgd
- Source and drain are symmetric diffusion terminals
  - By convention, source is terminal at lower voltage
  - Hence Vds  0
- nMOS body is grounded. First assume source is 0 too.
- Three regions of operation
  - Cutoff
  - Linear
  - Saturation

---
(a) ID versus VDS	(b) ID versus VGS for a fixed VDS
As VGS is made positive ID increases slowly at first and then much rapidly
ID reaches significant value (some predefined small ) at threshold voltage

---
I-V Characteristics
I-V Characteristics
Ids is dependent on both Vds and Vgs
In Linear region, Ids depends on
  - How much charge is in the channel?
  - How fast is the charge moving?

---
N channel Depletion mode FET
ON – No gate bias
N channel Depletion mode FET
ON – No gate bias
A channel is diffused between source and Drain

---
(- ve)
Channel Depletion with application of
negative voltage
- - - - - - - - - - - - - - -
+ + + + + + + + + + + + + + + +
- - - - - - - - - - - - - - - - - - - - - - - - - -
Induced +ve charge makes the channel less conductive
Causes effective depletion of majority carriers
Analogous to JFET characteristics
+ + + + + + + + + + + + + + +
 + + + + + + + + + + +
+ + + + +

---
N channel Depletion mode FET off
N channel Depletion mode FET off

---
nMOS Cutoff
nMOS Cutoff
- No channel
- Ids ≈ 0

---
nMOS Linear
nMOS Linear
- Channel forms
- Current flows from d to s
  - e- from s to d
- Ids increases with Vds
- Similar to linear resistor

---
nMOS Saturation
nMOS Saturation
- Channel pinches off
- Ids independent of Vds
- We say current saturates
- Similar to current source

---
N channel Depletion mode MOSFET
(a) ID versus VDS	(b) ID versus VGS for a fixed VDS
May be used for both enhancement and depletion mode
Lower threshold voltage than enhancement type

---
Switch using an N-channel enhancement-mode MOSFET.
Switch using an N-channel enhancement-mode MOSFET.

---
Types of MOSFET

---
Transfer characteristics (n channel FET)
D
G
S
Operating range decides the type of FET

---
Comparison between p- with n-channel FET
p-channel is easier to fabricate
n-channel is faster as the mobility of electrons is 3 times greater than the mobility of holes
n-channel takes less space

---
Classification scheme for field effect transistors
Classification scheme for field effect transistors