MOS INVERTERS

---
NMOS Inverter
Enhancement NMOS: (a) ID versus VDS	(b) ID versus VGS
Inverter Operation
- Plus signal input turns transistor on
- Ground is connected to output, thus a 1 (+) in gives 0 (Gnd) out
- A 0 input opens transistor and output is pulled high by resistor

---
NMOS Inverter
Resistor dissipates heat
Fabrication of resistor is not easy
Even modest values of Resistors occupy excessively large areas in silicon substrate

---
A transistor may be used as a resistor
VDD
Pull up
Output
Input
Pull down
In Pull down NMOS
For input=1, Pull down conducts
For input =0, Pull down is off

---
Pull up as an enhancement type NMOS
Pull up transistor input (VGG) should be high
VGG
Pull up
Output
Input
Pull down

---
Pull up as an enhancement NMOS
Vout
Vtpu
VGG
Pull up
Output
Input
Pull down
Non zero output
Vtpd
Vin
Dissipation is high since current flows when input=1
Vout can never be zero
Vout can never reach VDD (logical 1) if VGG=VDD as is normally the case
If VGG is higher than VDD, then an extra rail is required

---
Depletion type NMOS is used in pull up for better performance
Gate and Source is shorted to achieve VGS=0
In Pull down NMOS
For input=1, Pull down is on
For input =0, Pull down is off
Pull up is always on
Output
Input

---
Depletion type NMOS is used in pull up for better performance
Vout
No current
Output
Current flows
Input
Non zero output
Vtpd
Vin
Dissipation is high since current flows when input=1
Vout can never be zero

---
Drawbacks of Metal-gate MOS Transistors
Drawbacks of Metal-gate MOS Transistors
- High current flow for input at logic 1 in case of an inverter
- Excess surface state charges and mobile ion contamination cause the threshold variation.
- Vout never becomes exactly zero
- Suffer from excessive overlap capacitance.
- Parasitic capacitances Cgs and Cgd slow the transistor because they must be charged and discharged during switching.
- Aluminum is used as gate material which can erode completely causing contact spiking.

---
Types of MOSFET
Types of MOSFET
Pullup may be enhancement type PMOS

---
Complementary MOS Transistors (CMOS)
Complementary MOS Transistors (CMOS)
When A is pulled high (VDD), the PMOS inverter is turned off, while the NMOS is turned on pulling the output down to VSS
When A is pulled low (VSS), the NMOS inverter is turned off, while the PMOS is turned on pulling the output up to VDD
p
n
GND
A
Y = A'

---
Complementary MOS Transistors (CMOS)
Complementary MOS Transistors (CMOS)
Vout
p on
n off
n on
p off
Both on
Vtpd
Vin
No current flow either for logical 0 or for logical 1 inputs
Full logical 1 and 0 levels are presented at output
For devices of similar dimension p-channel is slower than n-channel device
p
n
GND
A
Y = A'

---
Complementary MOS Transistors (CMOS)
Complementary MOS Transistors (CMOS)
S
G
D
D
G
S
p
n
GND
A
Y = A'

---
CMOS Inverter Technology
CMOS Inverter Technology
- Complementary MOS, or CMOS, needs both PMOS and NMOS devices for their logic gates to be realized
- The concept of CMOS was introduced in 1963 by Wanlass and Sah, but it did not become common until the 1980’s as NMOS microprocessors were dissipating as much as 50 W and alternative design technique was needed
- CMOS still dominates digital IC design today

---
CMOS Inverter
CMOS Inverter
1. Circuit schematic for a CMOS inverter
2. Simplified operation model with a high input applied
3. Simplified operation model with a low input applied

---
Bipolar Technology	CMOS
Higher switching speed	Lower switching speed
It offers high power dissipation.	less power dissipation
low packing density.	high packing density
unidirectional device	Bi-directional capability (drain & source are interchangeable)
better noise performance	Weak noise performance
lower input impedance (high drive current)	High input impedance and low drive current.
It offers lower delay sensitivity to load.	It offers higher delay sensitivity to load (i.e. it has fan out limitation.)
It has higher trans-conductance,	It has lower trans-conductance,
higher manufacturing cost per device	low manufacturing cost per device.