PowerPoint Presentation
INVERTER- NMOS

---
- So far, we have treated transistors as ideal switches
- An ON transistor passes a finite amount of current
  - Depends on terminal voltages
  - Derive current-voltage (I-V) relationships
Transistor gate, source, drain all have capacitance
  - I = C (V/t) -> t = (C/I) V
  - Capacitance and current determine speed

---
Capacitance
Capacitance
- Any two conductors separated by an insulator have capacitance
- Gate to channel capacitor is very important
  - Creates channel charge necessary for operation
Source and drain have capacitance to body
  - Across reverse-biased diodes
  - Called diffusion capacitance because it is associated with source/drain diffusion

---
Gate Capacitance
Gate Capacitance
- Approximate channel as connected to source
- Cgs = oxWL/tox ,
  where εox= relative permittivity of insulation	ε0 = permittivity of free space
= CoxWL
Cox = gate capacitance per unit area
= ox/tox (fixed for fixed tox )

---
Channel Charge
Channel Charge
MOS structure looks like parallel plate capacitor while operating in inversions
  - Gate – oxide – channel
- Qchannel = CgsVgc
- C = Cgs = CoxWL,
Vgc depends on the position in the channel, let us take its average value as Vds/2
Effective gate voltage= Vgs – Vt , where Vt = threshold voltage
Vgc = (Vgs – Vt ) - Vds/2
Qchannel = Cox WL {(Vgs – Vt ) - Vds/2}
Where Cox =εoxε0 / tox

---
Carrier velocity
Carrier velocity
- Charge is carried by e-
- Electrons are propelled by the lateral electric field between source and drain
  - Eds = Vds/L
Carrier velocity v proportional to lateral E-field
v =  Eds	 called mobility
Time for carrier to cross channel:
t = L / v
= L/ Eds
= L2/ Vds

---
nMOS Linear I-V
nMOS Linear I-V
  Now we know
  - How much charge Qchannel is in the channel
Qchannel = Cox WL {(Vgs – Vt ) - Vds/2}
  - How much time t each carrier takes to cross
  t= L2/ Vds
Ids= Qchannel /t
= Cox (W/L) {(Vgs – Vt ) - Vds/2} Vds
= ( Cox /Z) {(Vgs – Vt ) - Vds/2} Vds where Z=L/W
= β {(Vgs – Vt ) - Vds/2} Vds
where β =  Cox /Z = Cox (W/L)
For small Vds, it may be considered negligible in comparison to Vgs-Vt
Ids = β(Vgs-Vt)Vds, a linear equation

---
nMOS Saturation I-V
nMOS Saturation I-V
If Vgd < Vt, channel pinches off near drain
  - When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current
Ids= β {(Vgs – Vt ) - Vdsat/2} Vdsat = β (Vgs – Vt )2/2
where β =  Cox /Z = Cox (W/L)
For a fixed Vgs, Ids is dependent on ratio L/W of transistor

---
nMOS I-V Summary
nMOS I-V Summary
Where

---
Example
Example
  - tox = 100 Å
  -  = 350 cm2/V sec
  - Vt = 0.7 V
Plot Ids vs. Vds
  - Vgs = 0, 1, 2, 3, 4, 5
  - Use W/L = 4/2

---
pMOS I-V
pMOS I-V
All dopings and voltages are inverted for pMOS
  - Source is the more positive terminal
Mobility p is determined by holes
  - Typically 2-3x lower than that of electrons n
  - 120 cm2/V•s in AMI 0.6 m process
Thus pMOS must be wider to
provide same current
  - In this class, assume
  n / p = 2.5

---
Ideal vs. Simulated nMOS I-V Plot
Ideal vs. Simulated nMOS I-V Plot
65 nm IBM process, VDD = 1.0 V

---
NMOS Inverter
Ids
Depletion type
Resistive
Vgs(dep)=0.3VDD
Saturation Vds>Vgs-Vt
Vgs(dep)=0
VDD
Vgs(dep)= - 0.1VDD
Vgs(dep)= - 0.3VDD
Vds
0.5VDD
VDD
Vout
Ids
Vgs(enh)=0.8VDD
Resistive
Vin
Saturation Vds>Vgs-Vt
Vgs(enh)=0.5VDD
Vgs(enh)=0.4VDD
Enhancement type
Vgs(enh)=0.2VDD
Vds
0.5VDD
VDD

---
NMOS Inverter
VDD
Ids
Vgs(enh)=0.8VDD
Vgs(enh)=0.5VDD
Vout
Vgs(dep)=0
Vgs(enh)=0.4VDD
Vin
Vgs(enh)=0.2VDD
Vds(enh)
0.5 VDD
VDD
Vds(dep)
Ids for both transistors must be equal
Depletion transistor must be always on (only Vgs=0 curve is relevant)
The points of intersection of the curves give points on transfer characteristics

---
NMOS Inverter :Transfer Characteristics
Ids
Vout
Vgs(enh)=0.8VDD
No current
VDD
Vgs(enh)=0.5VDD
Vin= Vout
Current
flows
Vgs(dep)=0
Vinv
Vgs(enh)=0.4VDD
Vgs(enh)=0.2VDD
Vds(enh)
Vds(dep)
Vtpd
VDD
Vin
The point at which Vin = Vout is denoted as Vinv

---
NMOS Inverter
Vout
VDD
VDD
Vin= Vout
Vout
Vinv
Vin
0.5 VDD
Vtpd
VDD
Vin
Transfer Characteristics varies with transistor parameters
Thus Vinv depends on the transistors being considered
For equal margins around the inverter threshold, let us set Vinv=0.5VDD. At this point, both transistors are in saturation.

---
Transistor parameters for an ideal inverter
VDD
Consider an arrangement where an inverter is driven by the input of another inverter
Vout
Vin
Vout
Vin
When Vinv=0.5VDD, both transistors are in saturation,
Ids =(μCox/Z)(Vgs-Vt)2 where Z=L/W
In pull up depletion transistor, Ids =(μCox/Zpu)(-Vtd)2/2 as Vgs=0
In pull down enhancement transistor, Ids =(μCox/Zpd)(Vinv-Vte)2/2
As both Idss are same, (Vinv-Vte)2 /Zpd = (-Vtd)2/Zpu
(-Vtd)2/(Vinv-Vte)2 = (Lpu/Wpu)/ (Lpd/Wpd) = Zpu/Zpd
Typical values: Vte=0.2Vdd, Vtd= -0.6Vdd, Vinv=0.5Vdd
Zpu/Zpd = 4

---
Ideal inverter
VDD
Vout
Vin
Vout
Vin
VDD
Vout
Vin= Vout
Zpu/Zpd = 4, for ideal condition
Where Z=L/W
It does not depend on the driver inverter
Zpu/Zpd =4
Decreasing Zpu/Zpd
Increasing Zpu/Zpd
0.5 VDD
VDD
Vin

---
Book to be followed
Book to be followed
Basic VLSI Design: Systems and Circuits
BY
Douglas A Pucknell
Kamran Eshraghian