PowerPoint Presentation
INVERTER- CMOS

---
CMOS INVERTER
- DC Response: Vout vs. Vin for a gate
- Ex: Inverter
  - When Vin = 0	->	Vout = VDD
  - When Vin = VDD	->	Vout = 0
  - In between, Vout depends on
  transistor size and current
  - Idsn = -Idsp
  - We could solve equations
  - But graphical solution gives more insight

---
I-V Characteristics
I-V Characteristics
Resistive region
Idsn= n Cox (Wn/Ln){(Vgs – Vtn) - Vds/2} Vds
Idsp= - p Cox (Wp/Lp){(Vgs – Vtp) - Vds/2} Vds
Saturation region
Idsn= n Cox (Wn/Ln) (Vgs – Vtn )2/2
Idsp= - p Cox (Wp/Lp) (Vgs – Vtp)2/2

---
Current vs. Vout, Vin
Current vs. Vout, Vin

---
DC Transfer Curve
DC Transfer Curve
Transcribe points onto Vin vs. Vout plot

---
CMOS Inverter: Operating Regions
CMOS Inverter: Operating Regions
Region	nMOS	pMOS
A	Cutoff	Linear
B	Saturation	Linear
C	Saturation	Saturation
D	Linear	Saturation
E	Linear	Cutoff
Current between rails
A
B
D
E
C
Vin

---
Current versus Vin
1
2
4
5
3
Current between rails
N Off
P On
No Current
P saturation
N resistive
N On
P Off
No Current
Vin > Vtn
N saturation
P resistive
Both in
saturation
Vin

---
CMOS INVERTER
Vout
VDD
Vin= Vout
Saturation region
Idsn= n (Vgs – Vtn )2/2 [n =n Cox (Wn/Ln) ]
Idsp= - p(Vgs – Vtp )2/2 [p =p Cox (Wp/Lp) ]
Vin
VDD
0.5 VDD
Vtpd
When both in saturation, Idsn= n (Vin -Vtn )2/2, Idsp= - p (Vin -VDD – Vtp )2/2
As Idsn= - Idsp, (Vin –VDD -Vtp ) / (Vin – Vtn) = - (n/p)1/2
Thus,	Vin = {VDD +Vtp +Vtn (n/p)1/2 }/ {1+(n/p)1/2}

---
CMOS INVERTER
Vout
VDD
Vin= Vout
Vin = {VDD +Vtp +Vtn (n/p)1/2 }/ {1+(n/p)1/2}
If n=p, and Vtp =-Vtn , then, Vin = VDD /2
Vin
VDD
0.5 VDD
Vtpd
For n=p, the change in logic levels is symmetrically disposed about the point at which Vin = Vout= VDD /2,
Thus for a good CMOS inverter, we need n=p
nCox (Wn/Ln)=p Cox (Wp/Lp) Wp/Lp =2.5(Wn/Ln) as n=2.5 p

---
Beta Ratio
Beta Ratio
- If p / n  1, switching point will move from VDD/2
- Called skewed gate
- Other gates: collapse into equivalent inverter

---
Book to be followed
Book to be followed
Basic VLSI Design: Systems and Circuits
BY
Douglas A Pucknell
Kamran Eshraghian