## Slide 1: Intel 8086 MICROPROCESSOR ARCHITECTURE
Assembly Language Programming
String, Procedure and Macro

## Slide 2: Outline
The 8086 String instructions
  Moving a String
  Using compare string byte to check password
Writing and using procedures
  The CALL and RET instructions
  The 8086 Stack
  Using PUSH and POP
  Passing parameters to and from procedures
  Writing and debugging program containing procedures
  Reentrant and Recursive procedures
  Writing and Calling Far procedures
  Accessing a procedure
Writing and using Assembler Macros
  Comparison Macros and Procedures
  Defining and calling a Macro without parameters
  Passing parameters to Macros

## Slide 3: The 8086 String instructions
A string is the series of bytes stored in successive memory locations.
Word processor or text editor programs can be used to create strings.
These programs have facility to search through the text.

## Slide 4: Moving a String(contd.)
Definition:
  You have a string of ASCII characters in successive memory locations in data segment, and you want to move the string to some new location in the data segment.
Basic pseudo code:
REPEAT
MOVE BYTE FROM SOURCE STRING
TO DESTINATION STRING
UNTIL ALL BYTES MOVED

## Slide 5: Moving a String(contd.)
The basic pseudo code doesn’t help much in understanding how the algorithm will be implemented.
Expanded code:
INITIALIZE SOURCE POINTER, SI
INITIALIZE DESTINATION POINTER, DI
INITIALIZE COUNTER, CX
REPEAT
COPY BYTE FROM SOURCE TO DESTINATION
INCREMENT SOURCE POINTER
INCREMENT DESTINATION POINTER
DECREMENT COUNTER
UNTIL COUNTER=0

## Slide 6: Using compare string byte to check password(contd.)
Definition:
  We want to compare a user entered password to the correct password stored in the memory. If the passwords do not match we want to sound an alarm and If the passwords matches we will allow access to computer for that user.
Need:
  REPEAT-UNTIL
  Compare String instruction CMPS

## Slide 7: Using compare string byte to check password - Code
Code:
INITIALIZE PORT DEVICE FOR OUTPUT
INTIALIZE SOURCE POINTER-SI
INITALIZE DESTINATION POINTER-DI
INITIALIZE COUNTER-CX
REPEAT
COMPARE SOURCE BYTE WITH DESTINATION BYTE
INCREMENT SOURCE POINTER
INCREMENT DESTINATION POINTER
DECREMENT COUNTER
UNTIL (STRING BYTES NOT EQUAL) OR (CX=0)
IF STRING BYTES NOT EQUAL THEN
SOUND ALARM
STOP
ELSE DO NEXT MAINLINE INSTRUCTION

## Slide 8: Writing and using procedures
• Avoid writing the same sequence of instruction again and again.
• Write it in a separate subprogram and call that subprogram whenever necessary.
• For that CALL instruction is used.

## Slide 9: The CALL and RET instructions(contd.)
The CALL Instruction:
Stores the address of the next instruction to be executed after the CALL instruction to stack. This address is called as the return address.
Then it changes the content of the instruction pointer register and in some cases the content of the code segment register to contain the starting address of the procedure.

## Slide 10: The CALL and RET instructions(contd.)
Chart for CALL and RET instruction 

## Slide 11: The CALL and RET instructions(contd.)
Types of CALL instructions:
DIRECT WITHIN-SEGMENT NEAR CALL: produce the starting address of the procedure by adding a 16-bit signed displacement to the contents of the instruction pointer.
INDIRECT WITHIN-SEGMENT NEAR CALL: the instruction pointer is replaced with the 16-bit value stored in the register or memory location.
THE DIRECT INTERSEGMENT FAR CALL: used when the called procedure is in different segment. The new value of the instruction pointer is written as bytes 2 and 3 of the instruction code. The low byte of the new IP value is written before the high byte.
THE INDIRECT INTERSEGMENT FAR CALL: replaces the instruction pointer and the contents of the segment register with the two 16-bit values from the memory.

## Slide 12: The CALL and RET instructions
The 8086 RET instruction:
When 8086 does near call it saves the instruction pointer value after the CALL instruction on to the stack.
RET at the end of the procedure copies this value from stack back to the instruction pointer (IP).

## Slide 13: The 8086 Stack
Section of memory you set aside for storing return addresses.
Also used to store the contents of the registers for the calling program while a procedure executes.
Hold data or address that will be acted upon by procedures.

## Slide 14: Using PUSH and POP
The PUSH register/memory instruction decrements the stack pointer by 2 and copies the contents of the specified 16-bit register or memory location to memory at the new top-of-stack location.
The POP register/memory instruction copies the word on the top-of-stack to the specified 16-bit register or memory location and increments the stack pointer by 2.

## Slide 15: Passing parameters to and from procedures
Major ways of passing parameters to and from a procedure:
In register
In dedicated memory locations accessed by name
With pointers passed in registers
With the stack

## Slide 16: Writing and debugging programs containing procedures
Carefully workout the overall structure of the program and break it down into modules which can easily be written as procedures.
Simulate each procedure with few instructions which simply pass test values to the mainline program. This is called as dummy or stubs.
Check that number of PUSH and POP operations are same.
Use breakpoints before CALL, RET and start of the program or any key points in the program.

## Slide 17: Reentrant and Recursive procedures
Reentrant procedures: The procedure which can be interrupted, used and “reentered” without losing or writing over anything.
Recursive procedure: It is the procedure which call itself.

## Slide 18: Writing and Calling Far procedures
It is the procedure that is located in a segment which has different name from the segment containing the CALL instruction.

## Slide 19: Accessing Procedure
Accessing a procedure in another segment
Put mainline program in one segment and all the procedures in different segment.
Using FAR calls the procedures can accessed as discuss above.
Accessing procedure and data in separate assembly module
Divide the program in the series of module.
The object code files of each module can be linked together.
In the module where variables or procedures are declared, you must use PUBLIC directive to let the linker know that it can be accessed from other modules.
In a module which calls procedure or accesses a variable in another module, you must use the EXTERN directive.

## Slide 20: Writing and using Assembler Macros

## Slide 21: Comparison Macros and Procedures
A big advantage of using procedures is that the machine codes for the group of instruction in the procedures needs to be loaded in to main memory only once.
Disadvantage using the procedures is the need for the stack.
A macro is the group of instruction we bracket and give a name to at the start of the program.
Using macro avoids the overhead time involved in calling and returning from a procedures.
Disadvantage is that this will make the program take up more memory than using a procedure.

## Slide 22: Defining and calling a Macro without parameters

## Slide 23: Passing parameters to Macros
The words NUMBER, SOURCE and DESTINATION are called as the dummy variables. When we call the macro, values from the calling statements will be put in the instruction in place of the dummies.